## Slide 1: Juniper Apstra 4.2.1 EVE-NG Virtual Lab Demo Video series companion guide Video 6: Day-1 Deploying Testing Hosts
Colin Doyle, Sr. CE AMER
See the complete video walkthrough on YouTube at: https://www.youtube.com/@5minutejunos
Ask questions at the Juniper Elevate Community using the hashtag #5minutejunos
Adapted from v4.0.0 documentation originally compiled by: - Raymond Lam, SSE APAC - Tony Chan, SSE APAC

## Slide 2
Agenda
Day-0 Fabric Onboarding
Virtual Device Profile Verification
Virtual Device Profile Cloning
Onboarding Virtual Nodes
Create ASN Pool and IP Pools
Create Logical Devices and Interface Maps
Create Rack Types
Create Templates
Create Blueprints
Day-1 Service Provisioning
Create Routing Zones
Create Virtual Networks
Assign Virtual Network to Switchports
Add Server Links
Data Center Interconnect
DCI Addendum: Direct Peering
Core/WAN Connectivity
Internet Connectivity
Day-2 Operational Scenarios
Incorrect Cable Patch (RCA, LLDP Link Discovery, Time Voyager)
Config Deviation Checking
Apply custom config through Configlet
View Telemetry Data
Hardware Replacement
Future Documentation
Firewall Service Chaining
  Cluster with Service Block
  Type-5 Route (fabric integrated) with MNHA
VLAN Stitching
vEvo Fabric
Prepping your Lab

## Slide 3: Day-1 Service Provisioning
Create Routing Zones
Create Virtual Networks
Assign Virtual Network to Switchports
Add Testing Hosts
Data Center Interconnect (OTT)
DCI Addendum – Direct Peering
Core Connectivity
Internet Connectivity

## Slide 4
In this section, we’ll boot and configure our vSRX LAG bridge nodes, our uMate hosts, and run some tests to verify connectivity.
Below diagram illustrates the topology of the data center after this section.
Add Testing Hosts
DC-A Blueprint
vn101 (192.168.101.0/24)
vn102 (192.168.102.0/24)
A-bms-3
A-bms-2
To A-leaf1
ge-0/0/9
To A-leaf2
ge-0/0/8
192.168.101.33
192.168.102.22
A-bms-1
192.168.101.11
To A-leaf1
ge-0/0/7
To A-leaf2
ge-0/0/7
To A-leaf1
ge-0/0/8
ae1
ae2
A-bms-1_bridge
A-bms-2_bridge
vSRX
uMate
vSRX
uMate
uMate
Tenant-1 Routing Zone
DC-B Blueprint
Tenant-1 Routing Zone
B-bms-1
192.168.101.44
To B-leaf1
ge-0/0/7
To B-leaf2
ge-0/0/7
ae1
B-bms-1_bridge
vSRX
uMate
B-bms-2
192.168.103.55
To B-leaf1
ge-0/0/8
To B-leaf2
ge-0/0/8
ae2
B-bms-2_bridge
vSRX
uMate
vn101 (192.168.101.0/24)
vn103 (192.168.103.0/24)

## Slide 5: Add Testing Hosts – Configure vSRX Nodes
Boot and configure A-BMS-1_Bridge, A-BMS-2_Bridge, B-BMS-1_Bridge, and B-BMS-2_Bridge vSRX nodes
Boot and configure A-BMS-1, A-BMS-2, A-BMS-3, B-BMS-1, and B-BMS-2 uMate hosts
Test reachability between uMate hosts

## Slide 6: Add Testing Hosts – Configure vSRX Nodes
Boot and configure A-BMS-1_Bridge, A-BMS-2_Bridge, B-BMS-1, and B-BMS-2 vSRX nodes
  A-BMS-1_Bridge
  Login with root, enter cli, and enter configuration mode
  set system root-authentication plain-text-password set password to Juniper
  set system host-name A-BMS-1_Bridge
  delete security
  set security forwarding-options family mpls mode packet-based
  set security forwarding-options family inet6 mode packet-based
  set interfaces ge-0/0/0 description A-BMS-1
  set interfaces ge-0/0/0.0 family ethernet-switching interface-mode access
  set interfaces ge-0/0/1 description ae1 gigether-options 802.3ad ae1
  copy interfaces ge-0/0/1 to ge-0/0/2
  set chassis aggregated-devices ethernet device-count 3
  set interfaces ae1 aggregated-ether-options lacp active
  set interfaces ae1.0 family ethernet-switching interface-mode access
  commit and-quit
  request system reboot at now
  Login with root/Juniper, enter cli, and check LACP with show lacp interfaces

## Slide 7: Add Testing Hosts – Configure vSRX Nodes
Boot and configure A-BMS-1_Bridge, A-BMS-2_Bridge, B-BMS-1, and B-BMS-2 vSRX nodes
  A-BMS-2_Bridge
  Login with root, enter cli, and enter configuration mode
  set system root-authentication plain-text-password set password to Juniper
  set system host-name A-BMS-2_Bridge
  delete security
  set security forwarding-options family mpls mode packet-based
  set security forwarding-options family inet6 mode packet-based
  set interfaces ge-0/0/0 description A-BMS-2
  set interfaces ge-0/0/0.0 family ethernet-switching interface-mode access
  set interfaces ge-0/0/1 description ae2 gigether-options 802.3ad ae2
  copy interfaces ge-0/0/1 to ge-0/0/2
  set chassis aggregated-devices ethernet device-count 3
  set interfaces ae2 aggregated-ether-options lacp active
  set interfaces ae2.0 family ethernet-switching interface-mode access
  commit and-quit
  request system reboot at now
  Login with root/Juniper, enter cli, and check LACP with show lacp interfaces

## Slide 8: Add Testing Hosts – Configure vSRX Nodes
Boot and configure A-BMS-1_Bridge, A-BMS-2_Bridge, B-BMS-1, and B-BMS-2 vSRX nodes
  B-BMS-1_Bridge
  Login with root, enter cli, and enter configuration mode
  set system root-authentication plain-text-password set password to Juniper
  set system host-name B-BMS-1_Bridge
  delete security
  set security forwarding-options family mpls mode packet-based
  set security forwarding-options family inet6 mode packet-based
  set interfaces ge-0/0/0 description B-BMS-1
  set interfaces ge-0/0/0.0 family ethernet-switching interface-mode access
  set interfaces ge-0/0/1 description ae1 gigether-options 802.3ad ae1
  copy interfaces ge-0/0/1 to ge-0/0/2
  set chassis aggregated-devices ethernet device-count 3
  set interfaces ae1 aggregated-ether-options lacp active
  set interfaces ae1.0 family ethernet-switching interface-mode access
  commit and-quit
  request system reboot at now
  Login with root/Juniper, enter cli, and check LACP with show lacp interfaces

## Slide 9: Add Testing Hosts – Configure vSRX Nodes
Boot and configure A-BMS-1_Bridge, A-BMS-2_Bridge, B-BMS-1, and B-BMS-2 vSRX nodes
  B-BMS-2_Bridge
  Login with root, enter cli, and enter configuration mode
  set system root-authentication plain-text-password set password to Juniper
  set system host-name B-BMS-2_Bridge
  delete security
  set security forwarding-options family mpls mode packet-based
  set security forwarding-options family inet6 mode packet-based
  set interfaces ge-0/0/0 description B-BMS-2
  set interfaces ge-0/0/0.0 family ethernet-switching interface-mode access
  set interfaces ge-0/0/1 description ae2 gigether-options 802.3ad ae2
  copy interfaces ge-0/0/1 to ge-0/0/2
  set chassis aggregated-devices ethernet device-count 3
  set interfaces ae2 aggregated-ether-options lacp active
  set interfaces ae2.0 family ethernet-switching interface-mode access
  commit and-quit
  request system reboot at now
  Login with root/Juniper, enter cli, and check LACP with show lacp interfaces

## Slide 10: Add Testing Hosts – Configure uMate Hosts
Boot and configure A-BMS-1_Bridge and A-BMS-2_Bridge vSRX nodes
Boot and configure A-BMS-1, A-BMS-2, A-BMS-3, B-BMS-1, and B-BMS-2 uMate hosts
Test reachability between uMate hosts

## Slide 11: Add Testing Hosts – Configure uMate Hosts
Boot A-BMS-1, A-BMS-2, A-BMS-3, B-BMS-1, and B-BMS-2 uMate hosts
  Configure hosts using the table below
  Login with user/Test123
  Edit ”Wired connection 1”
  Configure IPv4 Settings I intend to connect the lab to the public Internet so I’m including a public DNS server – you can change or omit as it suits your needs.
NOTE: I was seeing RFB errors until I set VNC_Viewer to “Picture quality = Medium” and “Scaling = Scale to fit window”.
Host Name | IP Address/CIDR | Default Gateway | Virtual Network (reference only)
A-BMS-1 | 192.168.101.11/24 | 192.168.101.1 | vn101
A-BMS-2 | 192.168.102.22/24 | 192.168.102.1 | vn102
A-BMS-3 | 192.168.101.33/24 | 192.168.101.1 | vn101
B-BMS-1 | 192.168.101.44/24 | 192.168.101.1 | vn101
B-BMS-2 | 192.168.103.55/24 | 192.168.103.1 | vn103

## Slide 12: Add Testing Hosts – Configure uMate Hosts
Boot A-BMS-1, A-BMS-2, A-BMS-3, B-BMS-1, and B-BMS-2 uMate hosts
  Configure hosts using the table below
  Login with user/Test123
  Edit ”Wired connection 1”
  Configure IPv4 Settings I intend to connect the lab to the public Internet so I’m including a public DNS server – you can change or omit as it suits your needs.
Host Name | IP Address/CIDR | Default Gateway | Virtual Network (reference only)
A-BMS-1 | 192.168.101.11/24 | 192.168.101.1 | vn101
A-BMS-2 | 192.168.102.22/24 | 192.168.102.1 | vn102
A-BMS-3 | 192.168.101.33/24 | 192.168.101.1 | vn101
B-BMS-1 | 192.168.101.44/24 | 192.168.101.1 | vn101
B-BMS-2 | 192.168.103.55/24 | 192.168.103.1 | vn103

## Slide 13: Add Testing Hosts – Configure uMate Hosts
Boot and configure A-BMS-1_Bridge and A-BMS-2_Bridge vSRX nodes
Boot and configure A-BMS-1, A-BMS-2, A-BMS-3, B-BMS-1, and B-BMS-2 uMate hosts
Test reachability between uMate hosts (within each fabric – inter-fabric testing will come at the end of the DCI section)

## Slide 14: Add Testing Hosts – Configure uMate Hosts
Test reachability between uMate hosts
  Open the MATE Terminal
  Ping the default gateway
  Ping between hosts within each fabric - we’ll test inter-fabric once we finish the DCI config in the next section
Host Name | IP Address/CIDR | Default Gateway | Virtual Network (reference only)
A-BMS-1 | 192.168.101.11/24 | 192.168.101.1 | vn101
A-BMS-2 | 192.168.102.22/24 | 192.168.102.1 | vn102
A-BMS-3 | 192.168.101.33/24 | 192.168.101.1 | vn101
B-BMS-1 | 192.168.101.44/24 | 192.168.101.1 | vn101
B-BMS-2 | 192.168.103.55/24 | 192.168.103.1 | vn103
NOTE: I like to drag the MATE Terminal icon to the desktop so it’s slightly faster to get to.

## Slide 15: Add Testing Hosts – Configure uMate Hosts
Test reachability between uMate hosts
  Open the MATE Terminal
  Ping the default gateway
  Ping between hosts within each fabric - we’ll test inter-fabric once we finish the DCI config in the next section
Host Name | IP Address/CIDR | Default Gateway | Virtual Network (reference only)
A-BMS-1 | 192.168.101.11/24 | 192.168.101.1 | vn101
A-BMS-2 | 192.168.102.22/24 | 192.168.102.1 | vn102
A-BMS-3 | 192.168.101.33/24 | 192.168.101.1 | vn101
B-BMS-1 | 192.168.101.44/24 | 192.168.101.1 | vn101
B-BMS-2 | 192.168.103.55/24 | 192.168.103.1 | vn103

## Slide 16: Add Testing Hosts – Configure uMate Hosts
Test reachability between uMate hosts
  Open the MATE Terminal
  Ping the default gateway
  Ping between hosts within each fabric - we’ll test inter-fabric once we finish the DCI config in the next section
Host Name | IP Address/CIDR | Default Gateway | Virtual Network (reference only)
A-BMS-1 | 192.168.101.11/24 | 192.168.101.1 | vn101
A-BMS-2 | 192.168.102.22/24 | 192.168.102.1 | vn102
A-BMS-3 | 192.168.101.33/24 | 192.168.101.1 | vn101
B-BMS-1 | 192.168.101.44/24 | 192.168.101.1 | vn101
B-BMS-2 | 192.168.103.55/24 | 192.168.103.1 | vn103